Shad

Hawaii is in the middle of the Pacific Ocean and as a result, we have cooling tradewinds.  In the olden days, people would leave the windows open and let the tradewinds naturally cool off the house, but now that home crimes are high, most people lock up their windows while away. Because the sun rises from the east and sets in the west, the eastern side of the house heats up in the morning and the western side heats up in the afternoon as direct sunlight hits the sides of the house. Today, more and more homes are using air conditioners.  Our robot is designed to reduce our reliance on fossil fuels which have to be imported, to make our islands more sustainable.

Our eco-friendly robot, Shad, reduces the temperature of a house by blocking some of the heat and glare off of the glass windows. Glass has a specific heat capacity of 0.84 J/gK so it heats up relatively fast.  As the sun heats up the windows, it heats up the room.  A locked house can be as hot as an oven.  Shad prevents this by rolling down a shade when the sun directly hits the window.  It uses a light sensor to detect light intensity and thereby know when the sunlight is directly hitting the window.  The robot consists of two (2) 269 motors to raise and lower the shade.  It also uses a winch driven by a 269 motor that is attached to a quadrature encoder that measures its rotation.  This determines how much the shade goes up or down, using the rope as a restraint.  A lamp was used to simulate the sun and a fan to simulate the tradewinds. The difference between the temperature in front of the shade and behind the shade can be as much as seven (7) degrees Celsius or 14 degrees Fahrenheit over five (5) minutes.  The shade is made of tank thread whose little holes let some air through but not the glare.  The air space between the shade and the window insulates the house from the heat.  As the sun rises above the house, the shade goes up and allows more of the natural trade winds through.

In 2010, 9% of home energy cost was spent on cooling.  Shad can reduce this amount.  Shad runs automatically so when at home, it will reduce glare and temperature while your windows are open.  It also allows more tradewinds to come in when direct sunlight isn’t hitting the window by pulling the shade up.

We read about using passive and active means to cool a building on the Autodesk Sustainability Workshop since Hawaii is normally hot.  Instead of using manmade materials for insulation, we decided on using a shade and an air space due to our cool tradewinds.